## Slide 1: Live HD.4K.8K over IP Networks. NOW
@ IBC 2018

## Slide 2: Lossless quality at lower bandwidth
Transparent quality to uncompressed or visually lossless
Robustness to multiple encoding generations
Robust to error
TICO – built to ease the move to IP

## Slide 3: Easy access to a wide range of resolutions
HD to 4K, 8K and beyond
4:2:0, 4:2:2, 4:4:4, raw, …
8, 10, 12, 14, 16 bit per components
TICO – built to ease the move to IP

## Slide 4: Optimized for Hardware & Software
Low FPGA resource usage
Real-time in software
Low memory (only line buffers), low power
TICO – built to ease the move to IP

## Slide 5: Low latency in Hardware and Software
Constant bitrate (CBR)
Few lines of pixels in hardware (Microsecond!!!)
Less than 1 frame latency in software
TICO – built to ease the move to IP

## Slide 6: A growing TICO family:
Formats | SMPTE RDD35 | JPEG XS (preliminary) | IP networks & SDI mapping examples
HD 720p60 /1080i60 | ~300 Mbps | 200 Mbps - 70 Mbps | 1 to x streams over 1GbE
HD 1080p60 | ~600 Mbps | 400 Mbps - 125 Mbps | 1 to x streams over 1GbE
4K 2160p60 | ~2,4 Gbps | 1,6 Gbps - 500 Mbps | 1 stream over 1GbE 1 to x streams over 10GbE Single 3G-SDI or HD-SDI
8K 4320p60 | ~8 Gbps | 6,4 Gbps - 2 Gbps | 1 to 4 streams over 10 GbE Single 12G-SDI
TICO – built to ease the move to IP

## Slide 7: Perfect in multi-generation response
TICO RDD35 quality after 10 coding generations (4:1)
TICO – built to ease the move to IP

## Slide 8: Multi-resolution transcoding
Extract lower resolution from the codestream at no processing cost
  Decode HD from 4K, Decode HD & 4K from 8K !
  Ease the editing, the monitoring & the distribution !
Original UHDTV
HDTV proxy
TICO
UHDTV-1 codestream
TICO – built to ease the move to IP

## Slide 9: Error resilience to a single bit flip
Error resilience is important in the case of transport over SDI in hybrid SDI / IP
With TICO, when a one-bit error occurs in 99% of the case only a few pixels of the final image are affected. It’s like uncompressed! The error propagation is limited!
TICO – built to ease the move to IP
Notes: In the graph, the original frame is compressed and one bit is flipped at 1000 different random positions in the compressed bitstream. These tampered bitstreams are then decompressed by the decoder.
The error propagation is limited thanks to its codestream syntax that has a clean split between raw data and coded data.

## Slide 10: Mathematically lossless mode available
Lossless coding is a de-facto feature. So if the expected compression ratio is not high (lower than 2:1), the results might be math. lossless.
To guarantee a CBR behavior, either padding, or rate allocation mechanisms will be applied to achieve the desired rate.
Typical UHDTV-1 60p 422 broadcast content will achieve about 7.5 Gbit/s in math. lossless. In other words, 12G-SDI down to a 10GbE with TICO could be lossless.
Chart: 
| EBU_Graphics.yuv10 | Earth-May_yuv10 | EBU_horse.yuv10 | kidssoccer.yuv10 | EBU_waterrocks.yuv10
profile
chrom
bpp
nlines
lossless
size_codestream
size_expected
uncompressed
TICO rate (Lossless) | 0.66585 | 0.34105 | 0.68343 | 0.69379 | 0.67179
Uncompressed rate | 1 | 1 | 1 | 1 | 1
Variable Bit Rate: Mathematically Lossless results (75% = 15bpp or 1.5:1)

## Slide 11: Open specifications & standardization
TICO SMPTE RDD35 specifies:
  TICO compression, its codestream syntax, its decoding process
  TICO bitstream mapping on SDI / ST2022-6
  TICO bitstream mapping on RTP
JPEG-XS (ISO/IEC 21122 DRAFT) specifies:
  Part 1: Core coding system (compression, codestream syntax and decoding process)
  Part 2: Profiles and buffer models
  Part 3: Transport and container with IETF draft
TICO – built to ease the move to IP

## Slide 12: IP & Hybrid SDI/IP Interoperability SDI & ST2022-6 mapping / rtp mapping for ST2110
TICO
(RDD35)
(JPEG-XS)
RTP Mapping
SDI Mapping
SMPTE
ST 2022-6
Compressed
IP Interface
Compressed
SDI interface
SMPTE
ST 2110-22
Bandwidth efficient IP workflow for HD/4K/8K
Current SDI workflow upgrade for 4K/8K
HD
4K
8K
TICO – built to ease the move to IP

## Slide 13: TICO Alliance supporting the JT-NM roadmap
Get MORE
from your existing SDI infrastructure
4K over a single 3G-SDI cable
8K over a single 12G-SDI cable
(…)

## Slide 14: TICO Alliance supporting the JT-NM roadmap
Get 4K
from your ST 2022-6 infrastructure
(…)

## Slide 15: TICO Alliance supporting the JT-NM roadmap
SIMPLIFY your Live IP production
Bandwidth efficient in HD, 4K & 8K over cost-effective networks

## Slide 16: TICO Alliance supporting the JT-NM roadmap

## Slide 17: IBC 2018 Demonstration participants
Complete ST2110 FPGA design
X10/X20 - Adaptable
IP-based Video Transport
ULTRA Series 4K/8K IP Codec & Converter
Teranex
Mini IP Video
VICO-4 - 4K TICO SDI converter. 4K transport over a single 3G-SDI in perfect quality and instantly
Virtuoso media function enables UHD/4K transport over 10GE/IP or 3G-SDI
Active Payload (ST2110-like) implementation of TICO over 10G Ethernet using Macnica’s VIPA™ PCIe card